## Slide 1: ADAU1466 Arduino Software
4/19/2023

## Slide 2: Overview
Same overall design as ADAU1701, except for the “ADAU1701 program” block.
For the ADAU1466, the program is put in the EEPROM by SigmaStudio

## Slide 3: Model View Controller
Inputs
(Views)
MQTT Message
Bluetooth BLE (UART)
Model
Outputs
(Views)
Status, allowable values and up/down management
MQTT Message
BLE messages
Serial Debugger
Command Execution
(“Controller”)
Volume
Input Selection
Crossover
EQ
Mute
Other DSP functions
Update_Model()
Execute_Command()
Serial Debugger
Update View()

## Slide 4: The Model
The Model defines the DSP functions and the current state of each function
  List of functions or capabilities:
  State of each function:
current value
default_value;
number_of_values;
pointer to table of value responses
Main_volume, Mute, Input, chan_vol_Tweeter, chan_vol_Woofer, chan_vol_Sub,
Delay_Tweeter, Delay_Woofer, BSC_freq, BSC_Gain,
Xover_TW_type, Xover_TW_freq,Xover_WS_type, Xover_WS_freq, EQ_50_Gain, EQ_80_Gain, EQ_300_Gain, EQ_600_Gain, EQ_900_Gain, EQ_2K_Gain,
EQ_5K_Gain, EQ_8K_Gain, EQ_13K_Gain, EQ_reset_Gain,
Rumble_filter_freq, Rumble_filter_Q, Bass_Enhancement_Mode, Peak_filter_freq, Peak_filter_Gain, SuperBass_freq, SuperBass_Intensity, SuperBass_Gain,
etc…

## Slide 5: Controller
The controller executes the commands.
Library functions are called to control the DSP:
  ADAU1466_cmd: Top-level functions for executing the commands
  ADAU1466_DSP: DSP functions such as filters and crossovers
  ADAU1466_Bilinear: Coefficient calculations for biquads
  ADAU1466_SPI: SPI communications and safeload
  ADAU1466_Lookup_tables: conversions for volume values, delays, Superbass routines
  ADAU1466_Shared_enums: enumerations for filter types and crossovers

## Slide 6: Views
Inputs: Serial Debugger, Bluetooth-LE or MQTT
  All inputs converted to Update_Model(command, value)
  Relatively easy to add a new class of inputs such as rotary encoders, IR remote, etc.
  HCI handler supports next/previous value commands to support navigation keys
Outputs: BT, debugger or MQTT messages
  Common output type: serial message that echoes command code and value from the Model table
  Other outputs are handled with device-specific code

## Slide 7: Initialization—out of date
Declarations
Define Structures
DSP: filters, Xover, Biquad, Coefficient struct
Nextion Display objects
ADAU1701 Init
Load ADAU1701 Program
(Prog_table in Arduino_shield.h)
Load ADAU1701 Parameters
(Param_table in Arduino_shield.h)
Menu & Display Init
Initialize HCI menu data
Init menu state
Load ADAU1701 Registers
CPU Init
Pins
Serial Ports
I2C (Wire)
SCI & HCI global variables
Cell Map Constants
Cell_map.ino
HCI Menu: field, page, menu
ADAU1701 memory tables
Arduino_shield.h
Files created by ASD program from SigmaStudio output
HCI Menu parameters and display values (constants)
Initialize display from menu
Set up callbacks for each display object

## Slide 8: User Input—Out of date
GUI Commands
Main Loop & callbacks
Bluetooth BLE
Check for activity on serial ports
SCI2
Callbacks
Check for IR signal
SCI
Wait for complete command
Determine command type and parameters
NexButtons
Update menu state
Update menu state
IR
Update menu state
Menu Commands
Echo menu cmd & display value to client
See “Update HW from Menu”
Menu-driven User Interface
See “Update HW from GUI”
The only user input source for the ADAU1466 program is the cell phone app.
This interface is Bluetooth BLE, with placeholders for MQTT or other WiFi protocol.
WiFi (MQTT)

## Slide 9: Update HW from Menu
Update HW from Menu
Branch on HCI field_ID
Main Volume
Delay (4)
Chan Vol (6 chans)
Xover Type (2)
Xover Freq (2)
Xover Polarity (2)
BSC Freq (1)
BSC Gain (1)
EQ Gain (9)
Look up actual volume from volume code
Look up actual volume from chan vol code
Look up actual delay from delay code
Update Crossover Object
Look up Biquad Spec (number, order, Q)
Calculate biquad coefficients
Set biquad to pass-through or -1
Set biquad to shelf filter @ freq and gain
Set peaking filter gain
Send formatted data to ADAU1701
Set up ADAU1701 registers for safe-write
Convert to ADAU1701 number (5.23)
Get Parameter address(es)
Biquad Safe Load
Each field_ID type has number of variants indicated by parentheses. Example: there are 4 field_ID’s for delay: Delay_L_Tweeter, Delay_R_Tweeter, Delay_L_Woofer, Delay_R_Woofer
Biquads are assigned in the Coefficient_calc routine
Note: Bass Enhancement and Custom Filters added 11/17/2017 but not shown on this diagram

## Slide 10: Serial Commands (Page 1)
Stereo Delay: Xssvv
Sub-cmd (ss) | Field_ID
0 | Delay_S_Tweet
1 | Delay_Tweeter
2 | Delay_Mid
3 | Delay_Woofer
(4) | Delay_Sub
Ex: “X0102” sets delay for tweeter to 3rd entry in table (.56”)
Commands use either a Command:Value or a Command:Subcommand:Value format. Command is a single ASCII character. Subcommand (and Value) use two ASCII characters to represent a Hex value 0-255. Three values are reserved: “FD” (hex for 253) reloads existing menu value; “FE” selects the previous value in the menu list; “FF” selects the next value in the menu table. The commands return the updated value back to the Bluetooth or WiFi host. If the client needs to interrogate the Arduino to know the current value, it should send a CssFD command, where C is the command and ss is the subcommand.
Volume: Zvv
Ex: “Z50” sets the volume to the 80th value in the table (0x50 = 80). The value of 80 is used as an index to the Main_Vol_table, which returns the ADAU1466 4-byte word that corresponds to 0 dB.
Ex: “ZFE” sets the volume to the previous value in the table), which is -1 dB. The return message to the client is “Z-1 ”
Stereo Chan Vol: Cssvv
Sub-cmd (ss) | Field_ID
0 | chan_vol_S_Tweet
1 | chan_vol_Tweeter
2 | chan_vol_Mid
3 | chan_vol_Woofer
4 | chan_vol_Sub
EQ: Essvv
Sub-cmd (ss) | Field_ID
0 | EQ_32_Gain
1 | EQ_64_Gain
2 | EQ_125_Gain
3 | EQ_250_Gain
4 | EQ_500_Gain
5 | EQ_1K_Gain
6 | EQ_2K_Gain
7 | EQ_4K_Gain
8 | EQ_8K_Gain
9 | EQ_16K_Gain
A | reset all EQ gains
() Delay Reference: Usually zero
Main Vol Code | Display Value
0, 1, 2,…85, 86 | -80, -79, -78, … +5, +6
Vol Code | Display Values
0 to 10 | -10, -9, -8, -7, -6, -5, -4, -3, -2, -1, 0
Delay | Display Values
0 to 11 | 0, .28, .56, .84, 1.13, 1.41, 1.69, 2.25, 2.81, 3.66, 4.78, 5.91
EQ Gain | Display Values
0 to 10 | -10dB, -8dB, -6dB, -4dB, -2dB, 0dB, +2dB, +4dB, +6dB, +8dB, +10dB

## Slide 11: Serial Commands (Page 2)
BSC: Bssvv
Sub-cmd (ss) | Field_ID
0 | BSC_Freq
1 | BSC_Gain
Xover: Fssvv
Sub-cmd (ss) | Field_ID
0 | Xover_ST-T_type
1 | Xover_ST-T_freq
2 | Xover_T_M_type
3 | Xover_T_M_freq
4 | Xover_M_W_type
5 | Xover_M_W_freq
6 | Xover_W_S_type
7 | Xover_W_S_freq
Save/Restore: Svv
Cmd (vv) | Field_ID
0 | Save (default block)
1 | save to block 1
2 | restore from block 1
3 | save to block 2
4 | restore from block 2
Input: Ivv
Sub-cmd (ss) | Field_ID
0 | Bluetooth (amp board)
1 | SPDIF (Wiim Mini)
2 | I2S
3 | Analog
ST-T Type: 0 to 5 | Display Values: None, B-W 1, B-W 3, L-R 2, L-R 4, L-R 8
ST-T Freq: 0 to 5 | Display Values: 3000, 4000, 5000, 6000, 7000, 8000
T-M Type: 0 to 5 | Display Values: None, B-W 1, B-W 3, L-R 2, L-R 4, L-R 8
T-M Freq: 0 to 5 | Display Values: 1000, 1500, 2000, 3000, 4000, 5000
M-W Type: 0 to 5 | Display Values: None, B-W 1, B-W 3, L-R 2, L-R 4, L-R 8
M-W Freq: 0 to 5 | Display Values: 300, 500, 750, 1000, 1500, 2000
W-S Type: 0 to 5 | Display Values: None, B-W 1, B-W 3, L-R 2, L-R 4, L-R 8
W-S Freq: 0 to 5 | Display Values: 80, 100, 120, 150, 200, 300
BSC Freq | Display Values
0 to 7 | 300Hz, 400Hz, 500Hz, 600Hz, 700Hz, 800Hz, 900Hz, 1.0KHz
BSC Gain | Display Values
0 to 6 | 0, 1, 2, 3, 4, 5, 6
Xover Polarity: Fssvv
Sub-cmd (ss) | Field_ID
8 | Xover_ST_polarity
9 | Xover_T_polarity
A | Xover_M_polarity
B | Xover_W_polarity
Polarity | Display Values
0 to 1 | +, -

## Slide 12: More Serial Commands (4/2023)
Bass Enh: Kssvv
Sub-cmd (ss) | Field_ID
0 | Rumble Freq
1 | Rumble Q
2 | Peak Freq
3 | Peak Gain
4 | Bass Enh Mode
5 | SuperBass_freq
6 | SuperBass_Intensity
7 | SuperBass_Gain
Custom Filters: Qssvv
Sub-cmd (ss) | Field_ID
0 | Shared1_Type
1 | Shared1_Freq
2 | Shared1_Q
3 | Shared1_Gain
4 | Shared2_Type
5 | Shared2_Freq
6 | Shared2_Q
7 | Shared2_Gain
8 | Tweeter_Type
9 | Tweeter_Freq
A | Tweeter_Q
B | Tweeter_Gain
C | Woofer_Type
D | Woofer_Freq
E | Woofer_Q
F | Woofer_Gain
10 (resp: G) | Sub_Type
11 (resp: H) | Sub_Freq
12 (resp: I) | Sub_Q
13 (resp: J) | Sub_Gain
14 (resp: K) | Clear All Filters
Curvature: Pssvv
Dipole Comp: Dxxvv
Shading: Rssvv

## Slide 13: Sigma Studio Interface
SigmaStudio (design DSP architecture)
Design used for Marthas:
5 stereo channels
    Left = front
    Right = back
Master Volume
Shared EQ
Volume trims & Polarity, each channel
10 biquads per chan
Delay for each channel
Compile to create output files:
XXX_param.h
ADAU1466 Arduino Tool
Create cell map file
Cell_map.ino
Maps the compiler-assigned Parameter RAM addresses to cell names so Arduino can program the DSP using symbolic names
Arduino IDE
Copy Cell_map.ino to sketch directory
Compile with other sketch files.

## Slide 14: SigmaStudio Design: Stereo 3-way

## Slide 15: SigmaStudio Design: 5x2/Dipole

## Slide 16: 5x2/Dipole
5 stereo channels with polarity control for L/R
  Polarity control allows 5-way monopole or 5-way dipole
10-band Equalizer, plus BSC and 2 shared filters
Supports 10-pole crossovers for most drivers
  Subwoofer crossover is 8-pole
Delay on all channels for driver offsets
Volume trim with mute for all channels
Bass management similar to subwoofer plate amp
  Rumble and Peaking filters
ADI Superbass algorithm
  Perceptual filter that adds overtones to give impression of deeper bass

## Slide 17: SigmaStudio Design: Line Array

## Slide 18: How to add a New Command
Example: Volume Bar Thickness
Insert command name in enums
  See enum.h (Thickness)
Add command code to Tables.h
  Add character to Command_table (“T”)
  Increment number_of_commands
Link command code to command name in SCI_BLE
  Example: case 'T’: cmd = Thickness; break;
Add command values to State_model
  (Model[Thickness] .xxx
  Add value list to Tables.h or use existing list (On_Off)
Add handler to Commands.ino
  Allows special processing for each command
Add values to Preferences as needed
  See Save_state in Save.ino
  See Restore_state, also

## Slide 19: Custom Filters
Custom Filters
Gain
Parameters
Q
Freq
Type
Options: Shared_1, Shared_2, Tweeter, Woofer, Sub
<<
>>
One_Pole_LP, One_Pole_HP, Two_Pole_LP, Two_Pole_HP, LP_Shelf, HP_Shelf, Bandpass, Notch, Peaking, All_Pass, None
Filter
Shared_1
Shared_2
Tweeter
Woofer
Sub

## Slide 20: Layout (as used in the Marthas)